## Slide 1
KNOWLEDGE COMPONENT: MODULE 2: KNOWLEDGE TOPIC 2: REWORK AND RECYCLING

## Slide 2: Introduction
Accurate monitoring and measurements allow calculations to be done to identify and eliminate losses.

## Slide 3: Calculations
The quantity of cane crushed is known since the transported cane passed a weighbridge. Imbibition water is measured or weighed, and mixed juice from the mill is weighed. From these three weights, the quantity of bagasse can be calculated:
Weight Cane + Weight imbibition water - Weight Mixed juice = Weight Bagasse
The sugar content of mixed juice and bagasse is analysed, so the quantities of sugar extracted from the cane and the sugar lost in bagasse are also known. The sum these two give sugar in cane, so:
POL mixed juice + POL bagasse = POL cane
From the quantity of bagasse and additional fuel, the boiler efficiency is calculated.
Of the sugar in mixed juice, part is lost in filtercake. The quantity can be calculated from the weight of filtercake and its sugar content.
Another part is lost in final molasses, this is also weighed and analysed.
The raw sugar is loaded in bulk tankers and weighed, before it is sent off to the sugar terminal or refinery.
When we compare the weight of sugar in mixed juice with the sum of sugar in filtercake, in final molasses and in the bagasse, there will always be a quantity of sugar unaccounted for.
This is called the undetermined loss or unknown loss.

## Slide 4: Acceptable losses
A loss of +/- 1% of sugar is considered normal
A sugar balance can be made from the calculations, as follows:
  Sucrose in Cane 100.0
  Sugar made 87.00
  Lost in bagasse 3.00
  Lost in filtercake 0.50
  Lost in final molasses 8.00
  Total of determined losses 11.50
  Undetermined loss 1.50
  Total losses 13.00
The two big sources of losses are final molasses and bagasse.

## Slide 5: Undetermined Losses
Chemical losses
  In the factory
  In the laboratory
Mechanical losses
  Leaks
  Discard of sugar-containing liquid
  Entrainment
Administrative losses

## Slide 6: Poor Monitoring and Losses
Poor monitoring of process flow and poor control of each of the steps in the process will result in greater undetermined losses because it will be unclear where the losses are taking place.
As shown above, losses can occur due to:
  Over flows and leaks
  Carry overs
  Recirculation of processed product
  Rework of substandard products.

## Slide 7: Losses are mainly dependant on time
All losses are very much dependent on the rate of processing the juices and molasses, hence the crushing rate.
  The faster the milling speed, the shorter the retention time of the different juices and molasses in the various vessels, resulting in less inversion, hence lower chemical (or undetermined) losses.
  The higher the overall time efficiency, the higher the overall recovery.
  In general the mechanical losses remain quite constant, so with a high crushing rate the pol input will be higher causing the mechanical losses to be relatively lower.
To enable the factory to keep losses to a minimum, accurate daily, weekly and monthly records need to be kept of all the samples, weights, sensors and gauges within every work station of the factory.
Samples taken along the process will be sent to the on-site laboratory for analysis and feedback to the process flow so that calculations can be done and adjustments to the process can be made if required.