## Slide 1
KNOWLEDGE COMPONENT: MODULE 7:
PAN BOILING: KT 5: PAN CONTROL AND AUTOMATION

## Slide 2: Importance of Pan Control
For good pan operation the following is important:
Constant pressure saturated steam at the required minimum pressure.
Batch pans are not conductive to steady steam pressure as their steam demand varies from 0 to maximum available.
Steam flow to the calandria is generally lower at the start of the cycle than at the end, as the viscosity increases and circulation rate decreases as the pan builds up.
Pan vacuum should be kept constant.
Fluctuations in the absolute pressure can result in changes to the level of supersaturation, which can lead either to false grain formation or crystal dissolution.
It is important to reduce the absolute pressure to as low a value as is practicable.
This is to reduce the temperature of the massecuites to avoid Maillard Reaction.
Note:
  Refinery pans > 20kPa abs.
  A-pans 17kPa abs.
  B- and C-pans 14kPa abs.

## Slide 3: Importance of Pan Control (cont.)
For good pan operation the following is important (cont.):
The higher the absolute pressure the higher will be the boiling point of the massecuite.
This results in faster crystallisation rates.
It also leads to higher sucrose losses and especially other undesirable reactions such as the Maillard reaction – hence the lower absolute pressure in the B- and C- pans where higher concentrations of impurities (such as reducing sugars and amino compounds which are the reactants in the Maillard reaction) occur.
The temperature of feed and/or water to the pan should be higher than that of the boiling massecuite.
This causes flashing as the feed enters the pan.
The brix of feed should be constant.

## Slide 4: Importance of Pan Control (cont.)
For good pan operation the following is important (cont.):
Feed to a pan may be added continuously or in slugs.
At first glance it would appear that continuous feeding would assist in giving steadier operation of a pan.
However if uniform distribution of feed in a pan is desired slug feeding should be more effective.
This is because slow continuous feed will all be distributed through the openings in the feed ring closest to the feed pipe entry, while full flow for short time intervals should be distributed through all the feed ring openings.
Unnecessary addition of hot water (movement water) to a pan is wasteful of steam and should be minimised.

## Slide 5: Importance of Pan Control (cont.)
For good pan operation the following is important (cont.):
Whenever pan automation is applied it is important to maintain manual checks.
The evaporation rate should be equal to or lower than the crystallisation rate in order to avoid the formation of false grain.
Although evaporation rate is often controlled in continuous pans because of the stable conditions, it is seldom controlled in batch boilings because of the wide variations in flow which depend on prevailing conditions.

## Slide 6: Pan Automation Using Conductivity
The aim of pan control is to keep the massecuite in the correct supersaturation zone during the boiling.
The supersaturation is controlled by controlling the brix of the solution.
Conductivity is used as a measure of the brix.
It is very important to carry out the whole process at constant temperature because supersaturation is effected by temperature.
To maintain the correct supersaturation using a conductivity curve as indicator of the brix increases during the growing phase, the temperature must be constant.
Different boilings utilise materials of different purities, hence the different boilings will have their own requirements in order to maintain the desired supersaturation i.e. each type of boiling (A-,B- and C- boilings) will have their own conductivity curve.

## Slide 7: Using Conductivity (cont.)
Conductivity is mostly used on lower grade boilings, for various reasons.
Although, like other indirect measurements, it has its disadvantages, like being influenced to a certain degree by grain content, its simplicity, fast measurement response and low cost make it very attractive.
Small incorrect influences on the conductivity are for a low grade massecuite of relatively small importance as the lower the purity of the massecuite the wider the metastable zone.
Conductivity cannot be used for high grade boilings (purity above 90) as the ash content is too low for reliable measurement and frequent control point changes will have to be made as opposed to low purity massecuites, where the set point may even remain unaltered for an entire crushing season.

## Slide 8: Using Computer Control
Modern pans are automated so that they require less frequent supervision by the pan boiler.
There are different methods to automate a pan, of which only two will be briefly discussed.
Method 1: Computer control
Method 2: Calcor Instruments

## Slide 9: Method 1: Computer Control
This method involves feeding a computer the required conductivity curve according to which the massecuite must be boiled.
This is done by entering different massecuite levels in the pan together with the required conductivity at each level.
As the pan boils the level of massecuite inside the pan rises.
Level sensors detect this rise in level.
As the level increases the computer varies the feed to the pan the so that the required conductivity is maintained.
In other words, as the level increases the conductivity set point changes.

## Slide 10: Method 1: Computer Control (cont.)
In practice the pan started is on manual control.
The steps involved are:
  washing the massecuite if necessary
  brixing to the required supersaturation for graining
  adding slurry.
The pan is then transferred to automatic control by the computer.
As the pan fills up the computer decreases the conductivity set points so that the brix of the liquor in the pan increases.
This is essential to maintain the correct level of supersaturation.
If the purity of the liquor and feed changes, the conductivity set points must be changed accordingly.

## Slide 11: Method 1: Computer Control (cont.)
If the purity of the material used decreases, the liquor must have higher brix valves to give the required supersaturation.
This is done by controlling the pan according to a lower conductivity curve.
If the purity of the material increases, the conductivity curve is raised.
The decrease in conductivity can thus be changed so that the pan is boiled at optimum ‘’tightness’ without forming false grain.
Instead of conductivity, radio frequently (RF) or boiling point elevation can be used as a measure of the brix the massecuite.
The principle is the same – the brix must increase as the pan level increases to maintain the correct supersaturation.

## Slide 12: Method 2: Calcor Instruments
Here the pan is fitted with 6 level probes.
A control panel is fitted with 5 conductivity control pods.
Each pod is activated at a certain level.
A pod is set with the brix that we wish the massecuite to have at that particular level.
Each conductivity pod is set using arbitrary valves between 0 and 10.
For example: for a B-massecuite
  At level 1, the pod is set at a value of 6
  At level 2, the pod is set at a value of 7
  At level 3, the pod is set at a value of 8
  At level 4, the pod is set at a value of 9
  At level 5, the pod is set at a value of 9.5
The Calcor controller thus senses the increased level in the pan and decreases the feed accordingly to achieve increase in the brix of the liquor.
The arbitrary pod settings are not actual brix values, but are related to brix values.

## Slide 13: Advantages of Automation
Faster boiling.
  This is because the optimum supersaturation coefficient can be maintained during boiling viz. high in the metastable zone but just below the intermediate zone.
  As a consequence better utilisation of equipment (pans) is achieved.
Improved quality of product.
  More regular crystals free of conglomerates and false grain is produced.