## Slide 1
KNOWLEDGE COMPONENT: MODULE 8:
CRYSTALLISATION, CENTRIFUGING AND DRYING:
KT 10: PROBLEMS EXPERIENCED DURING
CRYSTALLISATION AND SEPARATION

## Slide 2: Broken / Damaged Cooling Element
A broken/damaged element can cause water to leak into the massecuite.
This will be indicated by the purity of the mother liquor not decreasing satisfactorily during crystallisation.

## Slide 3: Cessation of Stirring
The stirring shaft can break or shear loose from the stirring elements or the stirring can cease due to some other reason.
This would lead to crystals settling to the bottom of the crystallisers.
In A-crystallisers especially crystal settling is rapid and a decision as to appropriate action must be taken within minutes i.e. resume/restore stirring or liquidate (empty) the crystallisers.

## Slide 4: Maillard Reaction
This is the worst important problem with pan floor operations.
Maillard reactions give bread crust its characteristic colour and texture.
It is very important in food processing because it gives colour, texture and taste.
Maillard reactions are a whole host of reactions that occur where glucose and amino nitrogen (-NH2) is present.
The amino nitrogen group occurs in amino acids and proteins.
The presence of glucose and amino nitrogen creates the potential for Maillard reactions, but heat and low water content (i.e. high concentration) is also required.

## Slide 5: Maillard Reaction
Maillard reactions are exothermic and produce heat which increases the rate of the reaction, which in turn produces more heat etc.
Apart from producing excessive amounts of heat, the Maillard reaction also produces CO2 gas.
In C-massecuite this causes foaming, swelling and overflow.
In addition the Maillard reaction forms colour and high viscosity products.
If allowed to proceed unchecked the Maillard reaction will carbonize the sugar.

## Slide 6: How will we know if the Maillard reaction has started?
The temperature will not cool to say +40°C in the crystalliser, but will increase to 70°C +.
The massecuite will start to foam and its volume will increase.
The increase in temperature cause crystals to dissolve and massecuite is also lost due to overflow.
Sucrose is thus lost chemically and physically.

## Slide 7: How can Maillard reactions be prevented?
Keep the temperature as low as possible.
This involves boiling water under higher vacuum.
Obviously viscosity limits this in practice.
Do not reduce the water content excessively.
This means lowering the brix by boiling less “tight” massecuites.
Lowering the brix from 97% to 95% increases the water content from 3% to 5%.
Increase the purity of the massecuite, since the Maillard reaction happens in impure solutions.
For example: C-massecuite should be at 55 purity and not 50.

## Slide 8: What can be done if a Maillard reaction has started?
Cool the massecuite by adding large amounts of dry ice or cold water.
Dilute the massecuite.
Add some chemicals.
These contain sulphur compounds e.g. NaHSO3 (sodium hydrogen sulphite) and Na2SO3 (sodium sulphite).
These have the ability to slow down some of the reaction involved.
The max amount of Na2SO3 is 400 ppm on massecuite.

## Slide 9: What do we usually do wrong that initiates a Maillard reaction?
A Maillard reaction normally starts in the hottest part of the C-station i.e. the C-pan.
If there is poor circulation and a “dead spot” gets hot, the Maillard reaction is started.
When the massecuite is dropped into the Strike receiver and moved to the crystallisers the Maillard reaction increases because of poor circulation.

## Slide 10: Evidence of the Maillard reaction
Let us compare syrup and final molasses.
The amount of Fructose remains high or even increases because of inversion occurring.
The amount of Glucose reduces because the Maillard reaction uses up glucose molecules.
If a final molasses sample is taken and analysed there is always a 30-40 % glucose loss.
This indicates that Maillard reactions are occurring but it normally remains controllable.