## Slide 1
KNOWLEDGE COMPONENT: MODULE 8:
CRYSTALLISATION, CENTRIFUGING AND DRYING:
KT 9: RAW SUGAR QUALITY

## Slide 2: Standards / Determinants
Parameter | Standard | Factors Affecting the parameter
Pol | ˃ 99.3% | Pan Boiling Crystallisation and Centrifuging
Colour | ˂ 1350 ICUMSA units | All unit operations especially Clarification, Pan Boiling and Centrifuging
Starch | ˂ 150 ppm | Cane
Fines | ˂ 35% | Pan Boiling & Sugar Drying
Moisture | ˂ 0.1% | Centrifuging & Drying
Ash | ˂ 0.2% | Pan Boiling & Centrifuging

## Slide 3: Export Sugar Penalty / Bonus
Parameter | Calculation | Example
Pol | 93.3% - Pol | 0.12% below specification = R1/ton
Colour | Colour - 1350 | 286 ICUMSA units above specification R1/ton
Starch | ppm - 150 | If starch is 67 ppm above specification = R1/ton
Fines | % Fines - 35 | If fines are 22% above specification = R1/ton